## Slide 1
软件 BIOS
Fast Video功能实现和应用

## Slide 2
Resource Allocate
VGA Device Init
Application
Introduction

## Slide 3
Resource Allocate
VGA Device Init
Application
Introduction

## Slide 4: Intruction
What is Fast Video（1）？
  Turn on display at an early stage (Pei Phase).
1
2

## Slide 5: Intruction
What Fast Video do ？
  Display Post Progress Bar
  Display Post Code

## Slide 6: Intruction
Fast Video
  方便查看机器当前的Post状态--（正常情况下显示设备初始化的阶段较晚）
  一种直观查看问题的Hang机点的方式--（可以通过fast video的post code判断）
  也可以通过Fast Video阶段显示输出一些其他的信息

## Slide 7
Resource Allocate
VGA Device Init
Application
Introduction

## Slide 8: Resource Allocate
GetCPURbBusNumAndFabricId
FabricGetAvailableResource-> PrefetchableMmioSizeBelow4G
PcdSet64(AmiPcdPeiPciMmioTopAddress,PciMmioStartAddress)
根据SocketNum，DieNum设置RbBusNum、FabricId
根据FabricResourceManagerServicesPpi获得
PciMmioStartAddress
准备工作

## Slide 9: Resource Allocate
InitDevices
EnumerateBus
CalculateBridgeResources
AssignBridgeResources

## Slide 10: Resource Allocate
Host Bridge
Root bridge
Device
P2P bridge
PEI阶段的枚举只会枚举显示设备，因为在会在读取设备信息的时候通过IsAllowedClassCodeDevice对设备进行筛选，只对vga设备进行枚举。
EnumerateBus
Bus号回填

## Slide 11: Resource Allocate
计算 32位 Base Address Register 的大小：
向Base Address Register每个bit写1， 得到32bit的数值，清除Encoding information bits(bit 1:0 for I/O, bit 3:0 for memory)，得到的数值取反 +1。

## Slide 12: Resource Allocate
Host Bridge
Root bridge
Device
P2P bridge
CalculateBridgeResources
Bridge上的资源为桥上所有设备的资源长度相加

## Slide 13: Resource Allocate

## Slide 14: Resource Allocate

## Slide 15: Resource Allocate
Host Bridge
Root bridge
Device
P2P bridge
AssignBridgeResources
*资源回收：在PCIBUS的第一步会将Pei阶段为BMC VGA分配的资源进行回收然后从新分配。

## Slide 16: Resource Allocate
Enable VGA-compatible IO

## Slide 17: Resource Allocate
Enable PCIE Root Bridge IO Decode To VGA-compatible Space

## Slide 18: Resource Allocate
FastVideoPeimEntryPoint
InitVGA
InitDevices
SetFrameBufferAddress
InitVGA_HW
SetMode
FBBltImage
GetCPURbBusNumAndFabricId
FabricGetAvailableResource-> PrefetchableMmioSizeBelow4G
PcdGetSetPciBridgeResources(get)
EnumerateBus
CalculateBridgeResources
AssignBridgeResources
PcdGetSetPciBridgeResources(set)
Enable VGA-compatible IO
Enable PCIE Root Bridge IO Decode To VGA-compatible Space
GetDevInfo

## Slide 19: Resource Allocate
CheckPreEnumerationInitFunctionHook
ASTInitFunc
ASTInitBridgeFunc
AmdBridgeInitFunc
AmdBridgeInitFunc
EnumerateBus(Bridge)
CheckPreEnumerationInitFunctionHook
Read->VendorId
Read->HeaderType
Write->PciBridgeInfoExt
EnumerateBus(Device’s under this Bridge)
Write->PciBridgeInfoExt.SubordinateBusNumber
EnumerateBus(Device)
CheckPreEnumerationInitFunctionHook
QueryPciDeviceResources
Read->RevisionId
IsAllowedClassCodeDevice

## Slide 20: Resource Allocate
QueryPciDeviceResources
Read->Bar.Offset Buffer32 & 1
check what type of resource
PciCfg->Write->Bar.Offset
PciCfg->Read->Bar.Offset
Get Length
CalculateBridgeResources

## Slide 21
Resource Allocate
VGA Device Init
Application
Introduction

## Slide 22: VGA Device Init

## Slide 23: VGA Device Init

## Slide 24: VGA Device Init
GetDevInfo
根据VID DID查找设备的配置空间，读取usRelocateIOBase、ulMMIOBase、ulMMIOSize、ulFBBase
并在InitVGA_HW中enable_vga

## Slide 25: VGA Device Init
enable_vga

## Slide 26: VGA Device Init
SetFrameBufferAddress
将ulFBBase的值赋给PCD变量，便于在后面使用时使用

## Slide 27: VGA Device Init
enable_vga
open_key
PLL_ Init
InitVGA
SetFrameBufferAddress
InitVGA_HW (Mem)
SetMode
FBBltImage
GetDevInfo
FindPCIDevice
InitVGA_HW (enable vga io access)
GetVRAMInfo
GetDRAMInfo
GetInfo(IOBase/MMIOBase)&Set MMIOSize

## Slide 28
Resource Allocate
VGA Device Init
Application
Introduction

## Slide 29: Application
PROGRESS_CODE(DXE_PCI_BUS_BEGIN);
LibReportStatusCode(EFI_PROGRESS_CODE, Code, 0, NULL, NULL)
StatusCodePtr->ReportStatusCode(Type,Value,Instance,CallerId,Data);
AmiReportStatusCode
SimpleStatusReport(PeiServices,Type,Value);
SimpleList
CheckPointStatus
CheckpointStatusReport
CheckpointList（Port80Checkpoint,ConOutCheckpoint,VGACheckPoint）
VGACheckPoint

## Slide 30: Application

## Slide 31: Application
Display Postcode

## Slide 32: Application
Display ProgressBar

## Slide 33: Application

## Slide 34: Q&A