## Slide 1
BIOS-肖志超
202108
SMBUS & SPD

## Slide 2
什么是SMBus
SMBUS的协议简介
如何访问SMBUS设备
SPD介绍
SMBUS & IIC

## Slide 3: 什么是SMBus
SMBUS 是 System Management Bus 的缩写，是1995年由Intel提出的，应用于PC系 统中的低速率通讯总线。 它主要是希望通过一条廉价并且功能强大的总线(由两条线组成)，来控制主板上的设备并收集相应的信息

## Slide 4: SMBUS的协议简介
SMBus Common AC specifications:
SMBus devices may support one of three different maximum bus speeds: 100 kHz,400 kHz, and 1 MHz.

## Slide 5: SMBUS的协议简介
SMBus 规范
Symbol | Parameters | 100 kHz Class |  | 400 kHz Class |  | 1 MHz Class |  | Units
 |  | Min | Max | Min | Max | Min | Max | 
fSMB | SMBus Operating Frequency | 10 | 100 | 10 | 400 | 10 | 1000 | kHz
tBUF | Bus free time between STOP and START Condition | 4.7 | – | 1.3 | – | 0.5 | – | µs
tHD:STA | Hold time after (REPEATED) START Condition | 4 | – | 0.6 | – | 0.26 | – | µs
tSU:STA | REPEATED START Condition setup time | 4.7 | – | 0.6 | – | 0.26 | – | µs
tSU:STO | STOP Condition setup time | 4 | – | 0.6 | – | 0.26 | – | µs
tHD:DAT | Data hold time | 0 | – | 0 | – | 0 | – | ns
tSU:DAT | Data setup time | 250 | – | 100 | – | 50 | – | ns
tTIMEOUT | Detect clock low timeout | 25 | 35 | 25 | 35 | 25 | 35 | ms
tLOW | Clock low period | 4.7 | – | 1.3 | – | 0.5 | – | µs
tHIGH | Clock high period | 4 | 50 | 0.6 | 50 | 0.26 | 50 | µs
tLOW:SEXT | Cumulative clock low extend time (slave device) | – | 25 | – | 25 | – | 25 | ms
tLOW:MEXT | Cumulative clock low extend time (master device) | – | 10 | – | 10 | – | 10 | ms
tF | Clock/Data Fall Time | – | 300 | – | 300 | – | 120 | ns
tR | Clock/Data Rise Time | – | 1000 | – | 300 | – | 120 | ns
tSPIKE | Noise spike suppression time | – | – | 0 | 50 | 0 | 50 | ns
tPOR | Time in which a device must be operational after power-on reset |  | 500 |  | 500 |  | 500 | ms

## Slide 6: SMBUS的协议简介
The Data Link Layer
1.Data validity

## Slide 7: SMBUS的协议简介
The Data Link Layer
The data on SMBDAT must be stable during the high period of the clock. Data can change state only when SMBCLK is low.

## Slide 8: SMBUS的协议简介
The Data Link Layer
START and STOP conditions
Two unique bus situations define a message START and STOP condition.
1. A HIGH to LOW transition of the SMBDAT line while SMBCLK is HIGH indicates a message START condition.
2. A LOW to HIGH transition of the SMBDAT line while SMBCLK is HIGH defines a message STOP condition. START and STOP conditions are always generated by the bus master. After a START condition the bus is considered to be busy. The bus becomes idle again after certain time following a STOP condition or after both the SMBCLK and SMBDAT lines remain high for more than tHIGH:MAX.

## Slide 9: SMBUS的协议简介
The Data Link Layer
START and STOP conditions

## Slide 10: SMBUS的协议简介
The Data Link Layer
Bus idle condition
Bus idle is the condition during which the SMBCLK and SMBDAT lines are both high, without any state transitions, for a time period specified as the minimum of the following: • tBUF from the last detected STOP condition or • tHIGH,MAX

## Slide 11: SMBUS的协议简介
The Data Link Layer
Data Transfers On SMBus

## Slide 12: SMBUS & IIC
The Data Link Layer
在一般运用下，I2C Bus与SMBus没有太大的差别，从实体接线上看也几乎无差异，甚至两者直接相连多半也能相安无误地正确互通并运作，但是还是存在些许不同的。
选项 | IIC | SMBUS
运作频率 | I2C此方面相当宽裕，最低频可至0Hz（直流状态，等於时间暂停），高可至100kHz（Standard Mode）、400kHz（Fast Mode）、乃至3.4MHz（High Speed Mode） | 最慢不慢於10kHz，最快不快於100kHz
协定机制 | 非必须（Acknowledge；ACK） | 必须（Acknowledge；ACK）

## Slide 13: 如何访问SMBUS设备
什么是SMBus设备

## Slide 14: 如何访问SMBUS设备
SMBus Host Controller 为CPU上SMBus系统的主设备。它的设备地址一般为Bus#00，Dev#14h，Fun#0
SMBus主设备

## Slide 15: SMBus主设备的访问方式
SMBus 寄存器空间可以通过如下两种方式访问：
1.IO方式 - SMB_BASE (Io-mappded base address) 2.Memory 映射方式 - SMBMBAR (mem-mapped base address)

## Slide 16: SMBus从设备 - SPD介绍
PC系统上, 常见的SMBUS从设备有clock generator, SPD(Serial Presence Detect ), 以 及笔记本电脑上的电池
SPD(Serial Presence Detect )是什么？
SPD数据提供内存通道上所有模块的关键信息，供系统BIOS使用，以便正确初始化和优化系统内存通道。 SPD eeprom的存储容量是有限的，因此使用了许多技术来优化这些字节的使用，包括覆盖和运行长度限制编码。
SMBus从设备

## Slide 17: SPD介绍
SPD 是什么

## Slide 18: SPD介绍
SPD 是什么

## Slide 19: SPD介绍
SPD 是什么

## Slide 20: SPD介绍
SPD -Serial Address Selection

## Slide 21: SPD介绍
SPD Address Map – DDR4
Standard Module Parameter - Overlay Bytes 128-191UDIMM/RDIMM/LRDIMM
Hybrid Module Parameters - Overlay Bytes 192 - 255 NVDIMM

## Slide 22: 扩展（SPD与CPU的连接方式）
非直接连接方式

## Slide 23: 作业
1.在DOS 环境下，通过汇编尝试访问一段SPD地址并打印数据